## Slide 1
HITACHI CONFIDENTIAL
Virtual Clamping Force

## Slide 2
Virtual method of determining the clamping force in a (smart) brake system
HITACHI CONFIDENTIAL
Anthony Ohazulike
Henning Sauerland
Massimiliano Lenardi
Hitachi Europe R&D Centre France
anthony.ohazulike@hitachi-eu.com
BRBU
(Astemo)
ACL
(European R&D)
Abdessamed Ramdane
Damian Janikowski
Advanced Engineering Brake Business Unit
abdessamed.ramdane@hitachiastemo.com
Progress meeting
28/11/2023

## Slide 3
HITACHI CONFIDENTIAL
Recap on Virtual Temperature Sensor

## Slide 4
HITACHI CONFIDENTIAL
Results on virtual temperature sensor

## Slide 5
HITACHI CONFIDENTIAL
Virtual Clamping Force Sensor for EMB

## Slide 6: Schematic diagram of the EMB system.

## Slide 7
Estimation of a (virtual) clamping force to be able to control the clamping of the brake accurately without force sensor.
Objective
Error range of +/- 500N or less
Target
Inaccurate target position estimation due to fixed mapping curve, which in reality, changes with many parameters.
Issue
AI can be used as a digital force sensor, reducing the amount of force sensors, hence reducing cost. PIML* creates the possibility that even less data can be used, and that output tends to adapt to the mechanics of the brake system.
Value
* Physics Informed Machine Learning
HITACHI CONFIDENTIAL

## Slide 8: Issues and solution
HITACHI CONFIDENTIAL
Current solution
Either control via deceleration control loop or Mapping (Target force vs. Rotor position)
Clamping force
Piston position
Clamping force
Piston position
mapping
Issue
Inaccurate target position estimation due to fixed mapping curve which in reality changes with many parameters.
Proposed solution
Solution that is driven by Artificial Intelligence (AI) Machine Learning and physics.

## Slide 9: Issues and solution
HITACHI CONFIDENTIAL
Benefits of the proposed solution
Solution is driven by Artificial Intelligence (AI) Machine Learning and physics
  Able to understand complex relationship of brake system parameters
  Force estimated based on many parameters for better accuracy
Eliminates one control loop (space for algorithm time execution improvement)
No need for physical temperature wear or force sensors
No similar solution exists in the market

## Slide 10
HITACHI CONFIDENTIAL
AI and Machine Learning (Data-driven) approach
Learning process
Pedal stroke/force
Current
Voltage
Speed
Disc Temperature
Pad/disc wear
Last Brake duration
Physic-based Clamping Force
…
Input (experimental data + more features from mathematical relations)
Feature selection
Relevant features
Data extraction
Learn the relationship
Implement
Feature selection
Relevant features
Data extraction
Learn the relationship
Implement
Neural network or any other ML/AI algorithm
Pedal stroke/force
Speed
Current (I)
Voltage (V)
I x V
Disc temperature
Pad/disc wear
…
…
Output
Input
Neural network or any other ML/AI algorithm
Clamping Force
Output
Learnt functions
Brake dynamo
Test car
Clamping force
Ground truth
Clamping Force
Ground truth
Clamping Force
AI-generated

## Slide 11
HITACHI CONFIDENTIAL
Pedal stroke/force
Current (I)
Voltage (V)
I x V
Disc temperature
Pad/disc wear
…
…
Input (real time data + feature engineered data)
Temperature Estimation
Output
Data extraction
and Feed
Temperature Estimation
Output
Data extraction
and Feed
Trained Neural network or any other ML/AI algorithm
Output
Clamping Force
Clamping force
AI and Machine Learning (Data-driven) approach
Deployment/execution process

## Slide 12: Remarks and Conclusion
Results show very high accuracy for CF <= 10,000N.
Still more data would be needed for high CF.
AI could learn some of the “unexplainable” clamping force behavior, which cannot be correctly estimated by the mapping.
PIML improved Data-only driven models.
Deployment workflow shows a latency of about 0.11ms within the target on MABX.
Clamping Force Estimation

## Slide 13
Notes: 本日は有難うございました。